## Slide 1: BEHAVIORAL MODELLING IN VERILOG
K.S.SAMBASIVARAO
Head,DEPARTMENT OF ELECTRONICS

## Slide 2: TOPICS:
Introduction
Structured Procedures
Procedural Assignments
Conditional Statement
Case Statement
Looping Statements
Timing Controls

## Slide 3: Introduction:
The behavioral modeling describes how the circuit should behave.
It is considered highest abstraction level as compared to data-flow or structured models.
In Verilog , Behavioral models contain procedural statements, which control the simulation and manipulate variables of the data types.
During the behavioral model simulation, all the flows defined by the always and initial statements start together at simulation time zero.

## Slide 4: Example:
module behave;
reg [1:0] a , b ; // a & b are 2-bit registers data types
initial //this statement is executed only once
begin
a = 2’b01; //a is initialized to 01
b = 2’b00; // b is initialized to 00
end
always //this statement is repeatedly executed
begin // simulation is completed
#50 a = ~a; //register a inverts every 50 time units
end
always
begin
#100 b = ~b; //register b inverts every 100 time units
end
endmodule

## Slide 5: Structured Procedures:
initial statement
always statement
task
functions

## Slide 6: Initial Statement
Activated at the beginning of simulation.
Executed once
initial
begin
a reg = 0; //initialize a register
for (index = 0; index<size; index = index +1)
memory[index] = 0; //initialize a memory
end
initial
begin
inputs = 6’b000000;
#10 inputs = 6’b001011;
#10 inputs = 6’b110001;
end

## Slide 7: Always Statement
Activated at the beginning of simulation.
Repeats continuously throughout the whole simulation run.
always
#100 clock = ~clock //creates a clock signal with #100 period time
always
@(posedge clock) //the block below starts execution at posedge of clock
begin
#10 a = 0; //#10 after the posedge of clock, a becomes 0
#20 b = 1; //#30 after the posedge of clock, b becomes 1
#40 b = 0; //#70 after the posedge of clock, b becomes 0
end

## Slide 8: Tasks
A Task that may or may not consume simulation time, returns values as output or inout argument type, and may or may not take arguments.
Keywords used: task and end task
Syntax:
task <task_name> (input <port_list>, inout <port_list>, output<port_list>);
….
endtask

## Slide 9: Functions
A function that does not consume simulation time, returns a single value or an expression, and may or may not take arguments.
Keywords used: function and endfunction.
Syntax:
function <return_type> <function_name>
….
return <value or expression>
endfunction

## Slide 10: Procedural Assignments:
Blocking procedural assignments: <lvalue>=<timing_control> <expression>
-- must be executed before the execution of the statements that follow them in a
sequential block
-- does not prevent the execution of statements that follow them in a parallel block
• Non-blocking procedural assignments: <lvalue><=<timing_control> <expression>
-- allow to schedule assignments without blocking the procedural flow
-- used whenever you want to make several register assignments within the same
time step without regard to order or dependance upon each other (e.g., register
swap)
-- they are executed in two steps: (a) the simulator evaluates the right-hand side,
(b) the assignment occurs at the end of the time step indicated by the
<timing_control>
• <timing_control> is optional in both cases
• It is possible to complete your project by using blocking only statements

## Slide 11: Example:
module block;
reg a, b, c, d, e, f;
initial begin
a = #10 1 ; // a is assigned at simulation time 10
b = #2 0; // b is assigned at simulation time 12
c = #4 1; // c is assigned at simulation time 16
end
initial begin
d <= #10 1; // d is assigned at simulation time 10
e <= #2 0; // e is assigned at simulation time 2
f <= #4 1; // f is assigned at simulation time 4
end
endmodule

## Slide 12: Conditional Statement:
• if (<expression>) <statement> else <statement>
• Equivalent to: if (<expression> != 0) <statement> else <statement>
• else-clause is optional and is always associated with the closest previous if that lacks an else
• Example
if (index > 0)
if (rega > regb)
result = rega;
else // else applies to preceding if
result = regb;

## Slide 13: Case Statement:
Case statement is a special multi-way decision statement:
reg [1:0] sel;
reg [15:0] in0, in1, in2, in3, out;
case (sel)
2'b00: out = in0;
2'b01: out = in1;
2'b10: out = in2;
2'b11: out = in3;
default out = 16'bx;
endcase
• The default statement is optional
• If all comparisons fail and the default is not given, none of the case statements is
executed

## Slide 14: Looping Statements:
Forever
Repeat
While
For

## Slide 15: Forever Statement
Continuously executes a statement.
Syntax:
<statement>
::=forever<statement>
||=forever
begin
<statement>+
end

## Slide 16: Repeat Statement
• Executes a statement a fixed number of times
Parameter size = 8, longsize = 16;
reg [size:1] opa, opb;
reg [longsize:1] result;
begin: mult // begin-end statements could optionally be named
reg [longsize:1] shift_opa, shift_opb;
shift_opa = opa;
shift_opb = opb;
result = 0;
repeat (size)
begin
if (shift_opb[1])
result = result + shift_opa;
shift_opa = shift_opa << 1;
shift_opb = shift_opb >> 1;
end
end

## Slide 17: While Statement
• Executes a statement until an expression becomes false
begin: count1s
reg [7:0] tempreg;
count = 0;
tempreg = rega;
while (tempreg)
begin
if (tempreg[0]) count = count + 1;
tempreg = tempreg >> 1;
end
end

## Slide 18: For Statement
Similar to C for-statement
for (initial_assignment; condition; step_assignment)
statement
• Using a for-loop to initialize a memory:
begin :init_mem
reg [7:0] tempi;
for (tempi = 0; tempi < memsize; tempi = tempi + 1)
memory[tempi] = 0;
end

## Slide 19: Timing Controls:
Delay control, which is introduced by the number symbol ( # ).
Event control, which is introduced by the at symbol ( @ ).
Wait statement, which operates like a combination of the event control and the while loop.

## Slide 20: Delay Control
Examples
#10 rega = regb;
#d rega = regb; //d is defined as a parameter
#((d+e)/2) rega = regb;
#regr regr = regr + 1; //delay is the value in regr

## Slide 21: Event Control
Synchronizes execution of a procedural statement with a value change on a net or
register, or the occurrence of a declared event
• Examples:
@r rega = regb; // controlled by any value changes in the register r
@(posedge clock) rega = regb; // controlled by positive edge on clock
forever @(negedge clock) rega = regb; // controlled by negative edge
@(trig or enable) rega = regb; // controlled by trig or enable
@(posedge clock_a or posedge clock_b) rega = regb;

## Slide 22: Wait Statement
The execution of a statement can be delayed until a condition becomes true
• The wait statement checks a condition: if it is false, causes the procedure to pause
until that condition becomes true before continuing
wait (condition_expression) statement
• Example:
reg enable, a, b;
initial begin
wait (!enable) #10 a = 1; // a becomes 1 at #110
#10 b = 1; // b becomes 1 at #120
end
initial
#100 enable = 0;

## Slide 23: THANK YOU