## Slide 1: BASIC ELECTRONICS
K.S.V.SAMBASIVARAO
HOD
DEPT. OF ELECTRONICS
PBSC COLLEGE Of A& S
VIJAYAWADA

## Slide 2: TRANSISTORS
A transistor is a semiconductor device used to amplify or switch electronic signals and electrical power. It is composed of semiconductor material usually with at least three terminals for connection to an external circuit.

## Slide 3: The three different transistor configurations are:
Common Base (CB)
Common Emitter(CE)
Common Collector(CC)

## Slide 4: Common Base(CB):
This transistor configuration provides a low input impedance while offering a high output impedance

## Slide 5: Common Collector(CC):
This transistor configuration has the collector terminal of the transistor common between the input and the output terminals . This offers high input impedance, low output impedance, voltage gain less than one and a large current gain

## Slide 6
In this configuration, the emitter terminal is common between the input and the output terminals . This configuration offers medium input impedance, medium output impedance, medium current gain and voltage gain.
Common Emitter(CE):

## Slide 7: FET(Field Effect Transistor):
FET is a transistor, where output current is controlled by electric field. FET sometimes, is called uni-polar transistor as it involves single carrier type operation. The basic types of FET transistor is completely different from BJT transistor basics.

## Slide 8
FET Conventional symbol types:

## Slide 9: Three terminals of FET:
Source (S): which the carriers enter the channel. Conventionally, current entering the channel at S is designated by IS.
Drain (D): which the carriers leave the channel. Conventionally, current entering the channel at D is designated by ID. Drain-to-source voltage is VDS.
Gate (G): The terminal that modulates the channel conductivity. By applying voltage to G, one can control ID.

## Slide 11: UJT (uni junction transistor ):
A unijunction transistor (UJT) is a three-lead electronic semiconductor device with only one junction that acts exclusively as an electrically controlled switch. The UJT is not used as a linear amplifier.

## Slide 12
UJT Symbol and Construction

## Slide 13: The value of the timing resistor, R3 is calculated as:
The time peroid is:

## Slide 14: Op-AMP(Operational Amplifier)
An operational amplifier (often op-amp or opamp) is a DC-coupled high-gain electronic voltage amplifier with a differential input and, usually, a single-ended output.

## Slide 15
Op Amps and Op Amp Circuits. ... Op amps are used in a wide variety of applications in electronics. Some of the more common applications are: as a voltage follower, selective inversion circuit, a current-to-voltage converter, active rectifier, integrator, a whole wide variety of filters, and a voltage comparator
The Voltage Gain (AV) of the operational amplifier can be found using the following formula
Applications of op-AMP:

## Slide 16: :
Operational Amplifiers Bandwidth:
The operational amplifiers bandwidth is the frequency range over which the voltage gain of the amplifier is above 70.7% or -3dB (where 0dB is the maximum) of its maximum output value as shown below.

## Slide 17: Block diagram of op-amp:

## Slide 18
Input stage
Mid stage
Level shifter
Output stage
Block diagram consists of 4 stages:

## Slide 19
Input stage:
It is having dual input and balanced output and used to provide voltage gain to an Op-Amp and it decides input resistance.
Mid stage:
It is having dual input and unbalanced output. It provides additional voltage gain to the input signal.
Level shifter:
In this emitter coupled logic circuit is used so that it provides the dc level to zero voltage level with respect to ground.
Output stage:
In this complimentary push pull circuit is used so that it provides low output resistance.

## Slide 20: Inverting amplifier:
Inverting Operational Amplifier. ... Negative Feedback is the process of “feeding back” a fraction of the output signal back to the input, but to make the feedback negative, we must feed it back to the negative or “inverting input” terminal of the op-ampusing an external Feedback Resistor called Rƒ.

## Slide 21: Non-inverting amplifier:
In this configuration, the input voltage signal, ( VIN ) is applied directly to the non-inverting ( + ) input terminal which means that the output gain of theamplifier becomes “Positive” in value in contrast to the “Inverting Amplifier” circuit we saw in the last tutorial whose output gain is negative in value.

## Slide 22: Op-amp Oscillator:
The Op-amp RC Oscillator. When used as RC oscillators, Operational Amplifier RC Oscillatorsare more common than their bipolar transistors counterparts.
The oscillator circuit consists of a negative-gain operational amplifier and a three section RC network that produces the 180o phase shift.

## Slide 23
THANK YOU